## Slide 1
AI SSD × HiCache 选型预研
给老板版: 结论、实验设计、IO 证据链与采购建议 | 2026-06-26
结论先行
BIWIN 系统盘路径最快
ZHITAI 是最佳独立 NTFS 数据盘
WDC 稳定居中
Seagate 有 bimodal 慢读风险
核心判断: 选型不能看普通 cold/warm,必须看 Phase7 replay + 多 run tail。
数据基础
• 7 phases + v3 mount-fixed 重跑
• Phase7 G: 6 run × 4 盘 = 24 replay 点
• fio 12 个硬件极限点
• iostat 1s 粒度 IO 画像
• 13 张 profiling 图

## Slide 2
Executive ranking: 6-run mean, not single-run peak
Selection-grade metric = replay_p0 mean + CV + IO diagnosis.

## Slide 3
Why the test is credible
The workflow deliberately separates cache validation, hardware ceiling, and real L3 reload.

## Slide 4
What the benchmark really measured
Normal cold/warm is an L2-hit test; Phase7 replay is the L3 SSD test.

## Slide 5
Single-run ranking is misleading
v3 alone made Seagate look fine; 6 runs expose its tail risk.

## Slide 6
IO diagnosis: HiCache replay is latency-bound
Replay is ~60-125KB reads, not a 1MB sequential fio workload.

## Slide 7
Disks are not saturated
Peak bandwidth is not the main bottleneck; p99 await and reader behavior dominate.

## Slide 8
Decision matrix
Recommendation uses observed latency, stability and IO behavior.

## Slide 9
Scorecard for purchase decision
Fastest path and best data SSD are different decisions.

## Slide 10
Recommended action
What to buy, what to avoid, what to test next.
BUY / USE
1. BIWIN as system/root L3 path when lowest latency matters
2. ZHITAI as preferred independent NTFS data SSD
3. WDC as stable capacity fallback
AVOID
Do not let Seagate alone carry tail-sensitive hot L3.
It had 3 slow runs around 3.4-3.5s out of 6.
NEXT
1. Trace Seagate slow reads with blk_mq + smartctl
2. Retest ZHITAI with drop_caches between runs
3. Test sglang 0.6+ page-size / reader changes
Executive takeaway: add host RAM first, then use ZHITAI/WDC for data L3; optimize reader/page-size before overpaying for peak SSD bandwidth.